## Slide 1
Activity Recognition & SOC Analysis
Optimizing On-Site EV Charging for Construction Equipment
Shubhan Mital
A69044961
MS in ECE - MLDS

## Slide 2
Research Objective
Data Collection
  Videos of construction site activities with electric vehicles
  State of Charge (SOC) data for each vehicle
  Tagging activities by minute for different vehicle types
Current Challenge
Problem: Charging EVs at a station and transporting to site is time-consuming
Solution: Bring portable charging stations to site (limited capacity)
Goal: Smart Charging Algorithm
Develop an algorithm that recommends optimal charging levels for each machine based on planned activities
Input: Work schedule → Output: Charge machine A to X%, machine B to Y%, etc.

## Slide 3
Current Progress
Completed Work
  Video Processing: Successfully split videos into 1-minute frames
  Timestamp Extraction: Captured overlayed timestamps from recordings
  Challenge Overcome: Handled multiple disjoint time segments from same day
  YOLOv8-based excavator detection implemented
  Deep SORT multi-object tracking integrated
  Motion-based idling state identification deployed
  End-to-end pipeline operational: Raw video → Detection → Tracking → Idle segments

## Slide 4
Step 1: Object Detection Using (YOLOv8)
Training (Model Development)
Manual image labeling → dataset creation
Train/Val/Test split defined in data.yaml
Base model: YOLOv8n (transfer learning)
Training Config: 50 epochs, Img size=480, batch=16, Pretrained weights
Output: best.pt (best-performing model saved automatically)
Inference (Video Processing)
Real-time detection at ~59 FPS, 480×480 input
YOLO NMS applied; highest-confidence excavator detection selected per frame
Confidence threshold used: >0.5
  Bounding boxes + confidence + class rendered on frames

## Slide 5
Step 1: Object Detection Using (YOLOv8)
CSV Output Format [frame id, x1, y1, x2, y2, confidence, class id]
Pixel-level bounding boxes
Frame-indexed detections
Single-class excavator identification
Final Artifacts
Trained model: best.pt
Detection log: detections.csv
Annotated video: Day-2 – YOLO.mp4

## Slide 6
Step 2: Multi-Object Tracking using Deep SORT
Algorithmic Framework
Deep SORT: motion + appearance-based tracking
Combines Kalman Filter (motion prediction) + CNN embeddings (appearance)
Detection–track assignment using Hungarian algorithm and IoU threshold = 0.7
Motion Model (Kalman Filter)
State vector: [u, v, γ, h, u̇, v̇, γ̇, ḣ] (bbox center, aspect ratio, height + velocities)
Constant-velocity assumption for prediction
Predictive update: x̂ₖ = F xₖ₋₁
Appearance Model (Deep Association Metric)
10-layer CNN generates 128-D appearance embedding
Cosine similarity for matching detections to existing tracks
Maintains appearance history for last 100 frames per track

## Slide 7
Step 2: Multi-Object Tracking using Deep SORT
Hyperparameters
Max-age = 35: Max frames a track survives without detection
N-init = 4: Frames needed before track is confirmed
Max-iou-distance = 0.7: IoU threshold for spatial matching
CSV Output Format [frame-id, track-id, x1, y1, x2, y2]
Persistent track-id across frames
Full temporal trajectory for each excavator
Handles occlusions up to max-age frames
Final Artifacts
Tracked video: Test-DEEPSORT.mp4
Tracking CSV: Track-Output.csv

## Slide 8
Step 3: Idling State Identification
Algorithmic Approach
Sliding window statistical feature extraction (Chen et al., 2020)
Analyze spatiotemporal invariance in bounding box properties
Feature 1: Centroid Displacement
Centroid, Euclidean displacement over window and Standard deviation
Feature 2: Bounding Box Area Variance
Area, Change of Area and Standard deviation threshold
Idling Decision Rule
Decide if process is idle or not
Signal Processing Pipeline
Smoothing: Savitzky-Golay filter (window=11, polyorder=2)
Denoising: Rolling median (window=5)
Segmentation: Sliding window (W=40 frames ≈ 0.68 sec)
Post-processing: Merge gaps <1 sec, discard <3 sec

## Slide 9
Step 3: Idling State Identification
Output Format (CSV) [track-id, start-frame, end-frame, duration-sec, start-time-sec, end-time-sec, start-HH:MM:SS, end-HH:MM:SS]
Provides per-track idling segments
Diagnostic visualizations: movement signal, area variance, binary idle timeline
Final Artifacts
CSV: Idling-segments.csv
Plots per track: movement & area with idle segments

## Slide 10
Next Steps - Activity Recognition & Productivity Analysis
Explore advanced activity recognition
Investigate 3D CNN frameworks (3D ResNet) for classifying excavator actions: Digging, Loading, Swinging, Idling
Research open-source implementations and pre-trained models for fine-tuning on construction datasets
Integrate with energy/SOC data
Link frame-by-frame activity labels with battery/SOC measurements
Build statistical profiles of energy consumption for each activity type
Identify activity-specific charge depletion rates
Develop productivity & charging optimization
Automatically compute cycle times and productivity metrics (LCY/hr)
Design charging recommendations based on planned activity schedule and station capacity
Optimize machine utilization while minimizing total charging time

## Slide 11
References
Chen, C., Zhu, Z., & Hammad, A. (2020). Automated excavators activity recognition and productivity analysis from construction site surveillance videos. Automation in Construction, 110, 103045. https://doi.org/10.1016/j.autcon.2019.103045
Redmon, J., Divvala, S., Girshick, R., & Farhadi, A. (2016). You Only Look Once: Unified, Real-Time Object Detection. https://arxiv.org/abs/1506.02640
Jocher, G., et al. (2023). Ultralytics YOLOv8 Documentation. Ultralytics. https://docs.ultralytics.com
Wojke, N., Bewley, A., & Paulus, D. (2017). Simple Online and Realtime Tracking with a Deep Association Metric. https://arxiv.org/abs/1703.07402
Bewley, A., Ge, Z., Ott, L., Ramos, F., & Upcroft, B. (2016). Simple Online and Realtime Tracking. https://arxiv.org/abs/1602.00763
Hara, K., Kataoka, H., & Satoh, Y. (2018). Can Spatiotemporal 3D CNNs Retrace the History of 2D CNNs and ImageNet? https://arxiv.org/abs/1711.09577
Savitzky, A., & Golay, M. J. E. (1964). Smoothing and Differentiation of Data by Simplified Least Squares Procedures. Analytical Chemistry, 36(8), 1627–1639. https://doi.org/10.1021/ac60214a047
SciPy Signal Processing Documentation. SciPy.org https://docs.scipy.org/doc/scipy/reference/signal.html